ORDINANCE NO. 83

AN ORDINANCE REGULATING THE USE OF PUBLIC AND PRIVATE SEWERS AND DRAINS, THE INSTALLATION AND CONNECTION OF BUILDING SEWERS, AND THE DISCHARGE OF WATER AND WASTES INTO THE PUBLIC SEWER SYSTEM; AND PROVIDING PENALTIES FOR VIOLATIONS OF SECTIONS THEREOF:  IN THE VILLAGE OF ALDEN.

BE IT ORDAINED BY THE COMMON COUNCIL OF THE VILLAGE OF ALDEN.

SECTION 1.  DEFINITIONS

Unless the context specifically indicates otherwise, the meaning of terms in this ordinance shall be as follows:

- “SEWAGE WORKS” shall mean all facilities for collecting, pumping, treating, and disposing of sewage.

- “SUPERINTENDENT” shall mean the Superintendent of the Municipal Sewage Works of the Village of Alden, or his authorized deputy, agent or representative.

- “INSPECTOR” shall mean the person or persons duly authorized by the City, to inspect and approve the installation of building sewers and their connection to the public sewer system.

- “SEWAGE” shall mean a combination of the water carried wastes from residences, business buildings, institutions, and industrial establishments, together with such ground, surface, and storm waters as may be present.

- “SEWER” shall mean a pipe or conduit for carrying sewage.

- “PUBLIC SEWER” shall mean a sewer in which all owners of abutting properties have equal rights, and is controlled by public authority.

- “COMBINED SEWER” shall mean a sewer receiving both surface runoff and sewage.

- “SANITARY SEWER” shall mean a sewer which carries sewage and to which storm, surface, and ground waters are not intentionally admitted.

- “INDUSTRIAL WASTES” shall mean the liquid wastes from industrial processes as distance from sanitary sewage.

- “BUILDING DRAIN” shall mean that part of the lowest horizontal piping of a drainage

system which receives the discharge from the soil, waste, and other drainage pipes inside the walls of the building and conveys it to the building sewer, beginning five (5) feet outside the inner face of the building wall.

- “BUILDING SEWER” shall mean the extension from the building drain to the public sewer or other place of disposal.

- “PERSON” shall mean any individual, firm, company association, society, corporation, or group.

- “SHALL” is mandatory:  “MAY” is permissive.

SECTION 2.  USE OF PUBLIC SEWERS REQUIRED

- It shall be unlawful for any person to place, deposit, or permit to be deposited in an unsanitary manner upon public or private property within the Village of Alden, or in any area under the jurisdiction of said Village, any human or animal excrement, garbage, or other objectionable waste which ordinarily would be regarded as sewage or industrial wastes.

CONTINUED

ORDINANCE NO. 83 – continued

- It shall be unlawful to discharge to any natural outlet within said Village, or in any area under the jurisdiction of said Village, any sanitary sewage, industrial waste, or other polluted waters, except where suitable treatment has been provided in accordance with subsequent provisions of this Ordinance.

- Except as hereinafter provided it shall be unlawful to construct or maintain any privy; privy vault, septic tank, cesspool or other facilities intended or used for the disposal of sewage.

- The owner of all houses, buildings or properties used for human occupancy, employment, recreation or other purposes situated within the Village and abutting any street, alley or right-of-way in which there is now located a public sewer or combined sewer of the Village, is hereby required at his expense to install suitable toilet facilities therein, and to connect such facilities directly with the proper public sewer in accordance with the provisions of this ordinance, within six months after date of official notice to do so, provided that said public sewer is within one hundred (100) feet of the property line.

SECTION 3.  PUBLIC SEWAGE DISPOSAL

- Where a public sanitary or combined sewer is not available under the provisions of SECTION 2-D, the building sewer shall be connected to a private sewage disposal system complying within all requirements of the State Board of Health.

- In such times as a public sewer becomes available to a property served by a sewage system as provided in SECTION 2-D, a direct connection shall be made to the public sewer in compliance with this ordinance, and any septic tanks, cesspools and similar private sewage disposal facilities shall be abandoned.

- The owner shall operate and maintain the private sewage disposal facilities in a sanitary manner at all times, at no expense to the Village.

- No statement contained in this article shall be construed to interfere with any additional requirements that may be imposed by the Village.

SECTION 4.  BUILDING SEWERS AND CONNECTIONS

- No unauthorized person shall uncover, make any connections with or opening into use, alter, or disturb any public sewer or appurtenances thereof, without first obtaining a written permit from the Village Clerk.  Before a permit may be issued for excavating for plumbing in any public street, way or alley, the person applying for such permit shall have executed unto the Village of Alden and deposited with the Village Clerk a corporate surety in the sum of $5,000.00 conditioned that he will perform faithfully all work with due care and skill, and in accordance with the laws, rules and regulations, established under the authority or any ordinances of the Village of Alden pertaining to plumbing.  This bond shall state that the person will indemnify and save harmless the Village of Alden and the owner of the premises against all damages, costs, expenses, outlays and claims of every nature and kind arising out of unskillfulness or negligence on his part in connection with plumbing or excavating for plumbing as prescribed in this ordinance.  Such bond shall remain in force and must be executed for a period of three (3) years except that on such

expiration it shall remain in force as to all penalties claims and demands that may have accrued there under prior to such expiration.

CONTINUED

ORDINANCE NO. 83 – continued

B.  There shall be two classes of building sewer permits:

  - for residential and commercial service, and

(2) for service to establishments producing waste.

In either case, the owner or his agent shall make application on a special form furnished by the said Village.  The permit application shall be supplemented by any plans, specifications, or other information considered pertinent in the judgment of the inspector.  A permit and inspection fee of Five ($5.00) for a residential or commercial building sewer permit and Ten dollars ($10.00) for an industrial building sewer permit shall be paid to the Village of Alden Clerk at the time the application is filed.

C.	All costs and expense incident to the installation and connection of the building sewer shall be borne by the owner.  The owner or person installing the building sewer for said owner shall indemnify the said Village from any loss or damage that may directly or indirectly be occasioned by said installation.

D.  A separate and independent building sewer shall be provided for every building; except where one building stands at the rear of another or an interior lot and no private sewer is available or can be constructed to the rear building through an adjoining alley, court, yard, or driveway, the building sewer from the front building may be extended to the rear building and the whole considered as one building sewer.  Other exceptions will be allowed only by special permission granted by the superintendent.

E.  Old building sewer or portions thereof, may be used in connection with new buildings only when they are found on examination and test by the said Inspector to meet all requirements of this ordinance.

F.  The building sewer shall be constructed of either Vitrified Clay Sewer Pipe and Fittings meeting the current A.S.T.M. Specifications for Standard or Extra Strength Clay Sewer Pipe or Extra Heavy Cast Iron Soil Pipe meeting the current A.S.T.M. Specifications or the Department of Commerce Commercial Standards for Extra Heavy Cast Iron Soil Pipe and Fittings.  If installed in filled or unstable ground, the building sewer shall be of Cast Iron Soil Pipe, except that vitrified clay pipe may be accepted if laid on a suitable improved bed or cradles as approved by the said Inspector.

G.  All joints and connections shall be made gas tight and watertight.  Vitrified clay sewer pipe shall be fitted with factory made Resilient Compression Joints meeting the A.S.T.M.

“Specifications for Vitrified Clay Pipe Joints having Resilient Properties.”  (Designation C425).

Before joining the pipe in the trench, the bell and spigot surfaces shall be wiped free of dirt or other foreign matter.  A lubricant or sealer as recommended by the pipe manufacturer shall be applied to the bell and spigot mating surfaces just before they are joined together.

The spigot end shall be positioned into the bell end of the pipe previously laid and shall then be shoved home to compress the joint and to assure a tight fit between the interfaces.

Joints for cast iron soil pipe shall be made by inserting a roll of hemp or jute and

thoroughly caulking it into place and then following with pure molten lead well

CONTINUED

ORDINANCE NO. 83 – continued

caulked, not less than one inch deep.  No paint, varnish or putty will be allowed in the joints until they have been tested and approved.

H.  The size and slope of the building sewer shall be subject to the approval of the said Inspector, but in no event shall the diameter of cast iron be less than four inches and clay tile less than 6 inches.  The slope of such four-inch pipe shall not be less than one-eighth inch per foot.  A slope of one-fourth inch per foot shall be used wherever practical.

I.   Whenever possible the building sewer shall be brought to the building at an elevation below the basement floor.  The depth shall be sufficient to afford protection from frost.  All excavations required for the installation of a building sewer shall be open trench work unless otherwise approved by said Inspector.  Pipe laying and backfill shall be performed in accordance with ASTM specifications (Designation C12) except that no backfill shall be placed until the work has been inspected by the Inspector or his representative.

J.   In all buildings in which any building drain is too low to permit gravity flow to the public sewer, sanitary sewage carried by such drains shall be lifted by approved artificial means and discharged to the building sewer.  No water operated sewage ejector shall be used.

K.  The connection of the building sewer into the public sewer shall be made at the “Y” branch designated for that property, if such branch is available at the suitable location.  Any connection not made at the designated “Y” branch in the main sewer, shall be made only as directed by the said Inspector, utilizing an appropriate pipe saddle with sealing collar.

L.  The applicant for the building sewer shall notify the said Inspector when the building sewer is ready for inspection and connection to the public sewer.  The connection shall be made under the supervision of the said Inspector or his representative.

M.  All excavations for building sewer installation shall be adequately guarded with barricades and lights so as to protect the public from hazard.  Streets, sidewalks, parkways and other public property disturbed in the course of the work shall be restored in a manner satisfactory to the said Council and Village.

SECTION 5.  USE OF PUBLIC SEWERS.

A.  No person shall discharge or cause to be discharged any storm water, surface water, ground water, roof runoff, subsurface drainage, cooling water or unpolluted industrial process waters to any sanitary sewer.

B.	No person shall discharge or cause to be discharged to any public sewer, any harmful waters or wastes, whether liquid, solid or gas, capable of causing obstruction to the flow in sewers, damage or hazard to structures, equipment and personnel of the sewage works, or other interference with the proper operation of the sewage works.

C.  The admission into the public sewers of any water or waters having harmful or objectionable characteristics shall be subject to the review and approval of the Superintendent, who may prescribe limits on the strength and character of these waters and wastes.  When necessary, in the opinion of the Superintendent, the owner shall provide at his expense, such preliminary treatment as may be necessary to treat these wastes prior to discharge to the public sewer.  Plans, specifications,

CONTINUED

ORDINANCE NO. 83 – continued

and any other pertinent information relating to proposed preliminary treatment facilities shall be submitted for the approval of the said Superintendent and the State Board of Health, and construction of such facilities shall

be commenced until said approval is obtained in writing.  Where preliminary treatment facilities are provided for any waters or wastes, they shall be maintained continuously in satisfactory and effective operation by the owner at his expense.

D.  When required by the Superintendent, the owner of any property served by a building sewer carrying industrial wastes shall install and maintain at his expense a suitable control manhole in the building sewer to facilitate observation sampling and measurement of the wastes.  All measurements, tests, and analyses of the characteristics of waters and wastes shall be determined in accordance with “Standard Methods for the Examination of Water and Sewage”, and shall be determined at the control manhole.  In the event that no special manhole has been required, the control manhole shall be considered to be the nearest downstream manhole in the public sewer to the point at which the building sewer is connected.

E.  Grease, oil, and sand interceptors shall be provided when, in the opinion of the said Inspector, they are necessary for the proper handling of liquid wastes containing grease in excessive amount, or any flammable wastes, sand, and other harmful ingredients except that such interceptors shall not be required for private living quarters or dwelling units.  Where installed, they shall be maintained by the owner, at his expenses, in continuously efficient operation at all times.

SECTION 6.  PROTECTION FROM DAMAGE.

No unauthorized person shall maliciously, willfully, or negligently break, damage, destroy, uncover, deface, or tamper with any structure, appurtenance, or equipment which is part of the municipal sewage works.  Any person violating this provision shall be subject to immediate arrest under charge of disorderly conduct.

SECTION 7.  POWERS AND AUTHORITY OF INSPECTORS.

The superintendent, inspector, and other duly authorized employees of the Village bearing proper credentials and identification shall be permitted to enter upon all properties for the purpose of inspection, observation, measurement, sampling, and testing, in accordance with the provisions of this Ordinance.

SECTION 8.  PENALTIES.

- Any person found to be violating any provision of this ordinance except Section 6 shall be served by the Village with written notice stating the nature of the violation and providing a reasonable time limit for the satisfactory correction thereof.  The offender shall, within the period of time stated in such notice, permanently cease all violations.

- Any person who shall continue any violation beyond the time limit provided for in Section 8-A., shall be guilty of a misdemeanor and upon conviction thereof, shall be fined in an amount no more than One Hundred dollars ($100.00) for each violation.  Each day in which any such violation shall continue shall be deemed a separate offense.

CONTINUED

ORDINANCE NO. 83 – continued

- Any person violating any of the provisions of this ordinance shall become liable to the Village for any expense, loss, or damage occasioned the Village by reason of such violation.

SECTION 9.  VALIDIT

- All ordinances or parts of ordinances in conflict herewith are hereby repealed.

- The invalidity of any section, clause, sentence, or provision of this ordinance shall not affect the validity of any other part of this ordinance which can be given effect without such invalid part or parts.

SECTION 10.  ORDINANCE IN FORCE.

This ordinance to be in full force and effect from and after its passage, approval and publication according to the law of the State of Minnesota.

Passed and approved on the 3rd day of July 1963.

R.F. SCHMIDT

Mayor

ATTEST:

A.G. ROLLINS

Clerk

12/04/63

Resolution pertaining to SEWER RENTAL, CHARGES AND DATE THEREOF was presented

RESOLUTION

Trustee Martinson presented the following resolution and moved its adoption.

WHEREAS; - It being to the best interests of the Village and to the users of the Sanitary Sewer System the following will apply:  All connections to said sewer system must be completed by July 1st, 1964.  That the charges for such sewer rental shall be 150% of the previous water bill, from December 15 to March 15 each year.  Payable with the water bill each quarter.  First billing will be from June 15 to Sept 15, 1964.  Payable on or before November 15, 1964 without penalty.  Trustee Hemmingsen seconded the motion for adoption.

Upon vote being taken there were 4 Yeas and no nays.  Motion adopted.